## Slide 1: Cutting Electricity Cost For Service Provider Networks
Muhammad Saqib Ilyas
FDC
Zartash Afzal Uzmi
Tariq Mahmood Jadoon
Ihsan Ayyub Qazi
Muhamad Fareed Zaffar
Aamir Qayyum

## Slide 2: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 3: Background
A YouTube data center
Source: http://bit.ly/1p07fEc
The Internet
Source: http://bit.ly/20pOBWJ
Source: http://cnet.co/1Q9SkZ0
Source: http://bit.ly/20pOYR1
Source: http://bit.ly/1KGJcsg
Cellular network
Federated networks empower communication

## Slide 4: Network Scale
1 Data Center ~ 50,000 - 80,000 servers
With great power comes
great electricity bills
Image source: http://bit.ly/1awWnLn
Google’s B4 SDN
Image Source: Jain et. al, “B4: Experience with a globally-deployed software defined WAN”, SIGCOMM 2013
Data Center
Inter Data Center Links
Massive infrastructure
Massive power draw
Google’s data center locations
http://bit.ly/1WbIvbe
Microsoft Azure’s data center locations
http://bit.ly/1mqvi26
Rich connectivity
Amazon
  87 data centers
  At least 2 M servers
Telenor Pakistan
  8000 cellular sites
4
Source: http://bit.ly/11erCWn
Source: http://bit.ly/1T9VBqd

## Slide 5: Motivation
$951 M
Source: datacenterknowledge.com
$143 M
Source: Greenberg et. al, “Cost of a cloud: Research Problems in Data Center Networks”, CCR 2009
Chart: 
| Others | Electricity Bill
 | 85 | 15
Electricity Bill
15%
Annual DC Opex
Electricity Cost
Chart: 
 | 50 | 50
Electricity Bill
Upto 50%
$81 M
Electricity Cost 2012
Source: GREENNETS
Significant electricity costs

## Slide 6: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 7: Opportunity
Most equipment (nearly) idle
Peaks and troughs quite pronounced
Deploy sufficient resources to handle peak
DC Idle power
75%-85% of peak power
Source: Emerson, “Energy Logic: Reducing Data Center Power Consumption…”
Opportunity for electricity cost savings
A. Nazir et. al, “Unveiling Facebook: a Measurement Study of Social Network Based Applications”
Barroso et. al, “The Case for Energy Proportional Computing”, IEEE Computer, 2007
Peng et. al, “Traffic-Driven Power Savings in Operational 3G Cellular Networks”, MOBICOM 2011
Workload
Power consumption (Watt)
Network workload has systematic variations
0
1
P
0.85P

## Slide 8
When workload rises even more …
Key Idea
TX
CA
Electricity price
$/MWh
Workload relocation (WR)
Least expensive
Workload relocation cuts electricity cost further
Resource pruning cuts electricity cost
NY
Data Center
52
72
122.4
Most expensive
As workload rises…
Deactivate idle equipment
Deactivate some equipment
Workload
CA: California
NY: New York
TX: Texas
Move workload from NY to TX
RP to save more
RP and WR can cut electricity costs
Ain’t no such thing as a free lunch
A. Qureshi et. al, “Plugging into energy market diversity”, HOTNETS 2008
Temporal diversity in electricity prices
Geographic diversity in electricity prices
Oregon cheaper
Texas cheaper
An Observation
Notes: Bigger. Photo of a real data center then zoom

## Slide 9: Transition Costs
Transition costs may be present
  Examples:
    Expensive inter data-center traffic
    Energy spent while resuming and sleeping
Relocate Energy Demand to Better Locations (RED-BL)

## Slide 10: This Thesis
Towards systematic minimization of network electricity cost
using Workload Relocation (WR) and Resource Pruning (RP)
while considering transition costs
Notes: Abbreviate. Single thesis statement
This thesis uses (boxes) WR and RP with consideration of relocation and (transition) costs by developing a systematic framework for electricity cost minimization

## Slide 11: Contributions
INFOCOM Mini-Conference 2012
Computer Networks, 2014
GLOBECOM 2013
Optimization framework
Simulation based evaluation
Adaptation of optimization framework
Simulation based evaluation
Finer granularity
NP-Completeness
NP-Hardness proof *
Additional evaluations
Submitted
* With the help of Dr. Mudassir Shabbir, ITU, Lahore
Data centers
Cellular Networks

## Slide 12: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 13: Case Study – I : Background
Data center operator
  Geographically distributed data centers
Data center equipment
Power consumed is affine function of workload
IT Load | Non-IT Load
Servers | Lighting
Storage | Cooling
Network | Power distribution
Source: http://bit.ly/1mrIi7o
Let’s recap how we can use WR and RP
Notes: Photo

## Slide 14: Problem Model
TX
NY
TX
NY
CA
TX
Interval - 1
Interval - 2
Interval - 3
CA
CA
NY
Network State
12
10
10
State Cost
Data center activation
Data center deactivation
8
6
Transition cost
Optimal State Trajectory Problem
Might not be globally optimal
TX
NY
CA
NY
CA
NY
14
12
12
4
0
CA
TX
TX
State cost locally suboptimal
Relocate Energy Demand to Better Locations (RED-BL)
Total cost: 42
Total cost: 46
Electricity price driven workload assignment
Sum of all data centers’ electricity cost
Locally optimal
An alternative workload mapping
State cost locally suboptimal
Transition costs lower than local optimal scheme
State cost locally suboptimal
No transition costs

## Slide 15: Optimization Formulation
Sum over all intervals
Sum over all data centers
Subject to several constraints (please see the thesis)
Transition energy
State energy
Workload
Data center capacity
Fraction of data center that is active
Unit price of electricity
Notes: Give the objective function and the constraints

## Slide 16: Experimental Setup
Workload from 3 popular Facebook apps
Electricity prices from 33 US locations
Simulated a week-long deployment plan
Compared RED-BL against various schemes
Notes: To evaluate RED-BL for geo-diverse data centers, we performed a simulation study which had the following setup. We used workload from three popular Facebook applications and normalized the cumulative workload. We verified that the characteristics of the cumulative workload resemble that of the workload for thousands of servers in a Google data center. We collected day-ahead electricity prices for 33 locations across the USA and simulated a weeklong deployment plan for the data centers situated at these locations. We compared RED-BL against a number of algorithms.

## Slide 17: Comparison Benchmarks
LO: Local Optimal Ignoring Transition Costs
LS: Local Optimal with Selection
UNIFORM: Equally distribute workload
3
3
1
15
15
20
0
0
2
2
2
1
1
3
2
1
2
1
3
2
3
3
1
15
10
10
4
6
2
1
2
1
3
2
3
3
1
12
10
10
0
0
Sometimes idling is better
Best practical variant of local optimal

## Slide 18: Cost Savings vs Over-provisioning
Overprovisioning (%)
Savings over UNIFORM (%)
Increased over provisioning
More capacity at cheaper locations
Greater savings
Returns start to “diminish”

## Slide 19: Electricity Cost vs Transition Cost
(De)activation overhead = energy cost
Electricity Cost Savings
vs UNIFORM (%)
Transition costs (relative magnitude)
No transition costs
Optimal energy savings scale well with transition costs
Notes: As the magnitude of transition overheads compared to the cost of handling workload increases, we see that the percentage savings in electricity cost decrease for all algorithms. RED-BL achieves close to the ideal lower bound electricity cost savings, whereas the best variants of the greedy algorithm scale worse than RED-BL.

## Slide 20: Granular (De)activation
Granularity of (de)activation
Can (de)activate half a data center
Can only (de)activate entire data center
Electricity Cost Savings Over
Full Data Center (De)Activation
Nearly linear increase in cost savings
Notes: Now, let’s see how RED-BL energy savings would improve if we allowed independent (de)activation of fixed size fractions of a data center. The extreme right handside of this graph represents the case where you can only (de)activate an entire data center at a time. This is 0% better than the standard “all or nothing” RED-BL, because it is the same thing. If we were able to (de)activate half a data center at a time, we could do about 2.5% better than standard RED-BL. If we were able to independently (de)activate 10% of a data center at a time, we could do 5% better than standard RED-BL. So, there is opportunity for greater savings with granular (de)activation and it has a linear trend.

## Slide 21: Summary – Case Study I
Electricity cost savings can be achieved
  Overprovisioning
  Diversity
It is important to consider transition costs
RED-BL has wider applicability

## Slide 22: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 23: Case Study II Cellular Networks
BSC
BSC
MSC
Major power consumers
TRXs
Power amplifiers
Air conditioning
Focus on BTSs to cut electricity cost
Source: GREENNETS Report, 2008
Marsan et. al, “Optimal Energy Savings in Cellular Access Networks”, ICC 2009
Notes: Give the motivating example to show that WR and RP can be used in cellular networks as well.

## Slide 24: Resource Pruning
Call volume
BTS Power Consumption (kW)
Power saving threshold (d)
Pmax
Pmin
Workload capacity
d
tmax
No. of calls ≤ d
Low call volume
Deactivate some TRXs
Resource Pruning cuts cost

## Slide 25: Does workload relocation help?
Assume that power saving is enabled if upto two calls are being served
Power saving
Power saving
Power saving
WR enables greater power savings

## Slide 26: Is Workload Relocation Possible?
40% users receive signal from more than three BTSs

## Slide 27: Optimization Formulation
For every interval, minimize # TRXs
Seemingly simple formulation
NP-Hard

## Slide 28: Experimental Setup
Call volume traces for 2 days at 26 urban BTSs
Trace driven simulation:
  Periodically obtain optimal call placement
  Place BTSs with low-traffic in power-saving mode

## Slide 29: BTS Power Consumption Models
Parameter | Value |  | 
 | Model 1 | Model 2 | Model 3
Idle Power (W) | 1425 | 2401.8 | 2341.5
Peak Power (W) | 1500 | 3887.5 | 2973.9
Power Saving per TRX (W) | 20 | 50 | 100

## Slide 30: Results: Power-Saving Feature Only
Energy savings | Model 1 | Model 2 | Model 3
Percentage | 4.73% | 5.43% | 12.89%
Daily energy savings (kWh) | 43.28 | 109.68 | 217.12
Country-wide daily savings -31000 sites (MWh) | 51.6 | 130.77 | 258.87

## Slide 31: Energy Savings (kWh) RP + WR
At least 9.8% lower power consumption
Number of re-optimizations in an hour
Average Daily Energy savings (kWh)

## Slide 32: Effect of Granular Deactivation
Granularity | Model 1 | Model 2 | Model 3
2-state | 5.38% | 6.29% | 14.94%
3-state | 6.81% | 7.73% | 18.62%
6-state | 8.70% | 9.65% | 23.37%
Savings increase with finer granularity

## Slide 33: Case Study II - Summary
Overlaps in signal coverage
  Some geo-flexibility in workload
Built-in power saving feature
Significant cost reduction through WR + RP

## Slide 34: Drawing Parallels With Case Study I
Parameter | Cellular network | Data centers
Network resource
Workload relocation
Resource pruning
Transition costs
TRX
Call hand off
Negligible
Servers
Client redirect
Server shutdown / idle / hibernate
(De)activation overheads
BTS Power Saving
Notes: Identify the similarities and differences between the two networks and observe how abstractions can be made.

## Slide 35: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 36: Future Work
Adaptation and application to 3G, 4G, 5G and beyond
Factor in other forms of transition costs:
  Cost of change in latency
  Cost of increase in call blocking probability
Experimentation on a real testbed
Incorporation into an OA&M framework
Interplay with energy markets

## Slide 37: Conclusions
RED-BL: an electricity cost reduction framework
  Systematic application of WR and RP
Can significantly reduce electricity costs
  Data centers
  Cellular networks
Reduction in power consumption
  Positive ecological impact

## Slide 38: Questions and Answers
If you can read this
Murphy’s law was violated

## Slide 39: List of Papers
Published:
  A simulation study of GELS for Ethernet over WAN, GLOBECOM 2007
  RED-BL: Energy solution for loading data centers, INFOCOM Mini-Conference, 2012
  Electricity cost efficient workload mapping, INFOCOM Computer Communications Workshop, 2013
  Low-Carb: Reducing energy consumption in operational cellular networks, GLOBECOM 2013
  RED-BL: Evaluating dynamic right sizing for data centers, Computer Networks, vol. 72, 2014
Submitted:
  Low-Carb: A practical scheme for improving energy efficiency in cellular networks

## Slide 40: Questions 1
Why not have one data center at the cheapest locations?
  There is no single cheapest location
  Diversity for:
    Disaster
    Latency

## Slide 41: Question 2
Why can’t DVFS be used?
  It can certainly be used
  It does not achieve fine grained energy proportionality
    Granularity of VF scaling is coarse
    Other components are also energy proportional

## Slide 42: Question 3
How many transitions in a day are likely?

## Slide 43: Question 4
How quick is a transition?

## Slide 44: DVFS Instead of Deactivation
Notes: If, instead of shutting down an entire data center, we switch the servers into lower-power mode using DVFS techniques, the power savings might reduce, but the scheme would be more agile to workload variations. Here, we see that the power consumption drops linear as the power consumption is lowered with DVFS. If the server power consumption drops to 10% of the peak, the data center power consumption would be reduced by about 70%. Another data point is that if we put all “idle” servers at 50% power consumption, we achieve about 20% power reduction.

## Slide 45: Reserve Margin
Notes: To be prepared for some stray workload at data centers which we planned to deactivate, we’ll keep some servers on as reserve. As we increase the amount of serving capacity in reserve mode, the difference in power consumption will increase compared to the scenario where we did not keep any reserve capacity.
Exactly how much “stray” traffic we receive can’t be predicted. In this chart, the lower line shows the situation where we don’t receive any stray traffic at all. The power consumption in that case is purely due to servers idling. The upper line represents the situation where we need all the reserve capacity for handling stray traffic. The actual situation may be somewhere in between.

## Slide 46: Results: Power-Saving + Handoff Absolute Energy Savings (%)

## Slide 47: Effect of Late Deactivation

## Slide 48: A Randomized Algorithm
Pick this
While there are BTSs in high-power mode
  Pick a random BTS
  For each call being handled by this BTS
    Hand-over to a candidate BTS in low-power mode
Nope
Nope
Yup!
Power saving
Power saving

## Slide 49: Performance of Heuristic Algorithm