## Slide 1: Cutting Electricity Cost For Service Provider Networks
Muhammad Saqib Ilyas
FDC
Zartash Afzal Uzmi (Advisor)
Tariq Mahmood Jadoon
Ihsan Ayyub Qazi
Muhamad Fareed Zaffar
Amir Qayyum

## Slide 2: Agenda
Background and motivation
Opportunity and methodology
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 3: Background
A YouTube data center
Source: http://bit.ly/1p07fEc
The Internet
Source: http://bit.ly/20pOBWJ
Source: http://cnet.co/1Q9SkZ0
Source: http://bit.ly/20pOYR1
Source: http://bit.ly/1KGJcsg
Cellular network
Federated networks enable communication

## Slide 4: Network Scale
Image source: http://bit.ly/1PqlC1V
Google’s data center locations
http://bit.ly/1WbIvbe
4
Source: http://bit.ly/11erCWn
Source: http://bit.ly/1T9VBqd
Amazon
  87 data centers
  At least 2 M servers
Telenor Pakistan
  8000 cellular sites
Geographic diversity

## Slide 5: A Challenge Due To Network Scale
Massive infrastructure
Massive power consumption
With great power comes
great electricity bills

## Slide 6: Motivation
$951 M
Source: datacenterknowledge.com
$143 M
Source: Greenberg et. al, “Cost of a cloud: Research Problems in Data Center Networks”, CCR 2009
Chart: 
| Others | Electricity Bill
 | 85 | 15
Electricity Bill
15%
Annual DC Opex (2011)
Electricity Cost
Chart: 
 | 50 | 50
Electricity Bill
Upto 50%
$81 M
Electricity Cost (2012)
Source: GREENNETS Report Summary (2014)
Network electricity costs are significant

## Slide 7: Agenda
Background and motivation
Opportunity and methodology
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 8: Opportunity
Most equipment (nearly) idle
Peaks and troughs quite pronounced
Deploy sufficient resources to handle peak
Data Center Idle Power
Between 75% and 85% of peak power
Source: Emerson, “Energy Logic: Reducing Data Center Power Consumption…”
Opportunity for electricity cost savings
A. Nazir et. al, “Unveiling Facebook: a Measurement Study of Social Network Based Applications”, ACM IMC 2008
Normalized Workload
Power consumption (Watt)
Systematic variations
0
1
P
0.85P
Lack energy proportionality
Week long workload from 3 popular Facebook applications
Barroso et. al, “The Case for Energy Proportional Computing”, IEEE Computer, 2007
Peng et. al, “Traffic-Driven Power Savings in Operational 3G Cellular Networks”, MOBICOM 2011

## Slide 9
Resource Pruning
TX
CA
NY
Data Center
Deactivate idle equipment
Deactivate some equipment
Workload
CA: California
NY: New York
TX: Texas
A. Qureshi et. al, “Plugging into energy market diversity”, HOTNETS 2008
Resource pruning cuts electricity cost
Notes: Bigger. Photo of a real data center then zoom

## Slide 10: Electricity Price Diversity
Oregon cheaper
Texas cheaper
Temporal diversity in electricity prices
Geographic diversity in electricity prices

## Slide 11: Workload Relocation
TX
CA
Electricity price
$/MWh
Workload relocation (WR)
Least expensive
Workload relocation cuts electricity cost
NY
52
72
122.4
Most expensive
CA: California
NY: New York
TX: Texas
Move workload from NY to TX
RP to save more

## Slide 12: Recap
Resource Pruning (RP) cuts electricity costs
Workload Relocation (WR) cuts electricity costs
Are WR and RP free?

## Slide 13: Transition Costs
Workload Relocation incurs cost of relocation
  Ex: Inter data-center traffic are often expensive
Resource Pruning incurs cost of (de)activation
  Ex: Time spent sleeping/hibernating

## Slide 14: This Thesis
Systematic minimization of network electricity cost using Workload Relocation and Resource Pruning while considering transition costs
Notes: Abbreviate. Single thesis statement
This thesis uses (boxes) WR and RP with consideration of relocation and (transition) costs by developing a systematic framework for electricity cost minimization

## Slide 15: Contributions
PUBLICATIONS
1- IEEE INFOCOM Mini-Conference, 2012
2- IEEE Computer Communications Workshop, 2013
3- Elsevier Computer Networks Journal, 2014
4- IEEE GLOBECOM, 2013
Optimization framework design
Evaluation using real world data from 3 large scale Facebook applications
Generalization of optimization framework to cellular networks
Analysis and evaluation using real world data
Data centers
Cellular Networks

## Slide 16: Agenda
Background and motivation
Opportunity and methodology
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 17: Case Study – I : Background
Data center operator
  Geographically distributed data centers
Data center equipment
Power consumed is a function of workload
IT Load | Non-IT Load
Servers | Lighting
Storage | Cooling
Network | Power distribution
Source: http://bit.ly/1mrIi7o
Notes: Photo

## Slide 18: Motivating Example
TX
NY
TX
NY
CA
TX
Interval - 1
Interval - 2
Interval - 3
CA
CA
NY
Network State
12
10
10
State Cost
Data center activation
Data center deactivation
8
6
Transition cost
Optimal State Trajectory Problem
Might not be globally optimal
TX
NY
CA
NY
CA
NY
14
12
12
4
0
CA
TX
TX
State cost locally suboptimal
Relocate Energy Demand to Better Locations (RED-BL)
Total cost: 42
Total cost: 46
Electricity price driven workload mapping
Sum of all data centers’ electricity cost
Locally optimal
An alternative workload mapping
State cost locally suboptimal
Transition costs lower than local optimal scheme
State cost locally suboptimal
No transition costs

## Slide 19: Optimization Formulation
Sum over all intervals
Sum over all data centers
Subject to several constraints (please see the thesis)
Transition energy
State energy
Workload
Data center capacity
Fraction of data center that is active
Unit price of electricity
Notes: Give the objective function and the constraints

## Slide 20: Experimental Setup
Workload from 3 popular Facebook apps
Electricity prices from 33 US locations
Simulated a week-long deployment plan
Compared RED-BL against various schemes
Notes: To evaluate RED-BL for geo-diverse data centers, we performed a simulation study which had the following setup. We used workload from three popular Facebook applications and normalized the cumulative workload. We verified that the characteristics of the cumulative workload resemble that of the workload for thousands of servers in a Google data center. We collected day-ahead electricity prices for 33 locations across the USA and simulated a weeklong deployment plan for the data centers situated at these locations. We compared RED-BL against a number of algorithms.

## Slide 21: Comparison Benchmarks
LO: Local Optimal Ignoring Transition Costs
LS: Local Optimal with Selection
UNIFORM: Equally distribute workload
3
3
1
15
15
20
0
0
2
2
2
1
1
3
2
1
2
1
3
2
3
3
1
15
10
10
4
6
2
1
2
1
3
2
3
3
1
12
10
10
0
0
Sometimes idling is better
Best practical variant of local optimal

## Slide 22: Cost Savings vs Over-provisioning
Over-provisioning (%)
Savings over UNIFORM (%)
Increased over-provisioning
More capacity at cheaper locations
Greater savings

## Slide 23: Electricity Cost vs Transition Cost
Transition cost = single interval idling
Electricity Cost Savings
vs UNIFORM (%)
Transition Costs (relative magnitude)
No transition costs
RED-BL energy savings scale well with transition costs
Notes: As the magnitude of transition overheads compared to the cost of handling workload increases, we see that the percentage savings in electricity cost decrease for all algorithms. RED-BL achieves close to the ideal lower bound electricity cost savings, whereas the best variants of the greedy algorithm scale worse than RED-BL.

## Slide 24: Granular (De)activation
Granularity of (de)activation
Can (de)activate half a data center
Can only (de)activate entire data center
Electricity Cost Savings Over
Full Data Center (De)Activation
Nearly linear increase in cost savings
Increasing granularity
Notes: Now, let’s see how RED-BL energy savings would improve if we allowed independent (de)activation of fixed size fractions of a data center. The extreme right handside of this graph represents the case where you can only (de)activate an entire data center at a time. This is 0% better than the standard “all or nothing” RED-BL, because it is the same thing. If we were able to (de)activate half a data center at a time, we could do about 2.5% better than standard RED-BL. If we were able to independently (de)activate 10% of a data center at a time, we could do 5% better than standard RED-BL. So, there is opportunity for greater savings with granular (de)activation and it has a linear trend.

## Slide 25: Summary – Case Study I
WR and RP are complementary
  Achieve electricity cost savings
Transition costs may be significant
  Must be considered in electricity cost optimization

## Slide 26: Agenda
Background and motivation
Opportunity and methodology
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 27: Case Study II Cellular Networks
BSC
BSC
MSC
Major power consumers
TRXs
Power amplifiers
Air conditioning
Focus on BTSs to cut electricity cost
Source: GREENNETS Report, 2008
Marsan et. al, “Optimal Energy Savings in Cellular Access Networks”, ICC 2009
Notes: Give the motivating example to show that WR and RP can be used in cellular networks as well.

## Slide 28: Resource Pruning
Call volume
BTS Power Consumption (kW)
Power saving threshold (d)
Pmax
Pmin
Workload capacity
d
tmax
Call volume ≤ d
Low call volume
Deactivate some TRXs
Resource Pruning cuts cost
BTS Power Saving mode

## Slide 29: Does Workload Relocation Apply?
Assume that power saving is enabled if upto two calls are being served
Power saving
Power saving
Power saving
WR enables greater power savings

## Slide 30: Coverage Diversity
~45% users receive signal from at least three BTSs

## Slide 31: Optimization Formulation
For every interval, minimize # TRXs
Seemingly simple formulation
NP-Hard

## Slide 32: Experimental Setup
Call volume traces for 2 days at 26 urban BTSs
Trace driven simulation:
  Periodically optimize call placement
  BTSs with low-traffic go to power-saving mode

## Slide 33: BTS Power Consumption Models
Parameter | Value |  | 
 | Model 1 | Model 2 | Model 3
Idle Power (W) | 1425 | 2401.8 | 2341.5
Peak Power (W) | 1500 | 3887.5 | 2973.9
Power Saving per TRX (W) | 20 | 50 | 100

## Slide 34: Results: Resource Pruning Only
Energy savings | Model 1 | Model 2 | Model 3
Percentage | 4.73% | 5.43% | 12.89%
Daily energy savings (kWh) | 43.28 | 109.68 | 217.12
Pakistan-wide daily savings 31000 sites (MWh) | 52 | 131 | 259
10 MW continuous power consumption

## Slide 35: Energy Savings (kWh) RP + WR
From 5%-15% lower power consumption
Number of re-optimizations in an hour
Average Daily Energy savings (kWh)

## Slide 36: Effect of Granular Deactivation
Granularity | Model 1 | Model 2 | Model 3
2-state | 5.38% | 6.29% | 14.94%
3-state | 6.81% | 7.73% | 18.62%
6-state | 8.70% | 9.65% | 23.37%
Savings increase with finer granularity
All TRXs independently controllable
Two halves of the TRXs independently controllable
Increasing granularity

## Slide 37: Case Study II - Summary
Average user in range of multiple BTSs
  Workload relocation can be leveraged
Resource Pruning: Built-in feature
Significant cost reduction through WR + RP

## Slide 38: Drawing Parallels With Case Study I
Parameter | Cellular network | Data centers
Network resource
Workload relocation
Resource pruning
Transition costs
TRX
Call hand off
Negligible
Servers
Client redirect
Server shutdown / idle / hibernate
(De)activation overheads
BTS Power Saving
Notes: Identify the similarities and differences between the two networks and observe how abstractions can be made.

## Slide 39: Agenda
Background and motivation
Opportunity and methodology
Case studies:
  Data centers
  Cellular networks
Conclusions and future work

## Slide 40: Future Work
Adaptation and application to 3G and beyond
Factor in other forms of transition costs:
  Change in latency
  Increase in call blocking probability
Experimentation on a real testbed
Interplay with energy markets

## Slide 41: Conclusions
RED-BL: an electricity cost reduction framework
  Systematic application of WR and RP
Can significantly reduce electricity costs
  Data centers
  Cellular networks
Reduction in power consumption
  Positive ecological impact

## Slide 42: Acknowledgements
Dr. Fahad
Dr. Mudassir
Dr. Fareed
Dr. Tariq
Dr. Naveed
Dr. Adnan
Dr. Jahan
Dr. Chen-Nee
Saqib Raza
Dr. Atif
Reviewers
Fellow PhD Students
My parents
My family
My wife
Encouragement
Guidance
Feedback
Dr. Zartash
Dr. Ihsan
Dr. Sohaib
Prayers
Datasets
Dr. Atif
Dr. Bilal

## Slide 43: Acknowledgements
Speechless
Questions and Answers
Areeha
Areeba
Fatima

## Slide 44: List of Papers
Published:
  A simulation study of GELS for Ethernet over WAN, GLOBECOM 2007
  RED-BL: Energy solution for loading data centers, INFOCOM Mini-Conference, 2012
  Electricity cost efficient workload mapping, INFOCOM Computer Communications Workshop, 2013
  Low-Carb: Reducing energy consumption in operational cellular networks, GLOBECOM 2013
  RED-BL: Evaluating dynamic right sizing for data centers, Computer Networks, vol. 72, 2014
Submitted:
  Low-Carb: A practical scheme for improving energy efficiency in cellular networks

## Slide 45: Questions 1
Why not have one data center at the cheapest locations?
  There is no single cheapest location
  Diversity for:
    Disaster
    Latency

## Slide 46: Question 2
Why can’t DVFS be used?
  It can certainly be used
  It does not achieve fine grained energy proportionality
    Granularity of VF scaling is coarse
    Other components are also energy proportional

## Slide 47: Question 3
How many transitions in a day are likely?

## Slide 48: Question 4
How quick is a transition?

## Slide 49: DVFS Instead of Deactivation
Notes: If, instead of shutting down an entire data center, we switch the servers into lower-power mode using DVFS techniques, the power savings might reduce, but the scheme would be more agile to workload variations. Here, we see that the power consumption drops linear as the power consumption is lowered with DVFS. If the server power consumption drops to 10% of the peak, the data center power consumption would be reduced by about 70%. Another data point is that if we put all “idle” servers at 50% power consumption, we achieve about 20% power reduction.

## Slide 50: Reserve Margin
Notes: To be prepared for some stray workload at data centers which we planned to deactivate, we’ll keep some servers on as reserve. As we increase the amount of serving capacity in reserve mode, the difference in power consumption will increase compared to the scenario where we did not keep any reserve capacity.
Exactly how much “stray” traffic we receive can’t be predicted. In this chart, the lower line shows the situation where we don’t receive any stray traffic at all. The power consumption in that case is purely due to servers idling. The upper line represents the situation where we need all the reserve capacity for handling stray traffic. The actual situation may be somewhere in between.

## Slide 51: Results: Power-Saving + Handoff Absolute Energy Savings (%)

## Slide 52: Effect of Late Deactivation

## Slide 53: A Randomized Algorithm
Pick this
While there are BTSs in high-power mode
  Pick a random BTS
  For each call being handled by this BTS
    Hand-over to a candidate BTS in low-power mode
Nope
Nope
Yup!
Power saving
Power saving

## Slide 54: Performance of Heuristic Algorithm