## Slide 1: Cutting Electricity Cost For Service Provider Networks
Muhammad Saqib Ilyas
FDC
Zartash Afzal Uzmi
Tariq Mahmood Jadoon
Ihsan Ayyub Qazi
Muhamad Fareed Zaffar
Aamir Qayyum

## Slide 2: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers (e.g., Facebook and Google)
  Cellular networks (e.g., Sprint and Verizon)
Conclusions and future work

## Slide 3: Background
A YouTube data center
Source: youtube.com
The Internet
Source: freeimages.com
Source: cnet.com
Source: sekho.com.pk
Source: flaticon.com
Source: vcetsiras.blogspot.com
Federated networks empower communication

## Slide 4: Network Scale
Parameter | Microsoft | Amazon | Google
Servers | Millions | 2.8 – 5.6 M | 900000
Data Centers | > 26 | ~ 87 | 14
1 Data Center ~ 50,000 - 80,000 servers
Telenor: 8000 cell sites
With great power comes
great electricity bills
Image source: http://bit.ly/1awWnLn
Google’s B4 SDN
Image Source: Jain et. al, “B4: Experience with a globally-deployed software defined WAN”
Data Center
Inter Data Center Links
Massive infrastructure
Massive power draw
Google’s data center locations
http://bit.ly/1WbIvbe
Microsoft Azure’s data center locations
http://bit.ly/1mqvi26
Rich connectivity

## Slide 5: Motivation
$951 M
Source: datacenterknowledge.com
$143 M
Source: Greenberg et. al, “Cost of a cloud: Research Problems in Data Center Networks”, CCR 2009
Chart: 
| Others | Electricity Bill
 | 85 | 15
Electricity Bill
15%
Annual DC Opex
Electricity Cost
Chart: 
 | 50 | 50
Electricity Bill
Upto 50%
$81 M
Electricity Cost 2012
Source: GREENNETS
Significant electricity costs

## Slide 6: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers (e.g., Facebook and Google)
  Cellular networks (e.g., Sprint and Verizon)
Conclusions and future work

## Slide 7: Opportunity
Time
Traffic Volume
Network provisioned according to peak
Most equipment (nearly) idle
Peak and trough are quite pronounced
Google: Enough servers, storage and bw to handle peak
DC Idle power
75%-85% of peak power
Source: Emerson, “Energy Logic: Reducing Data Center Power Consumption…”
Opportunity for electricity cost savings
Barroso et. al, “The Case for Energy Proportional Computing”, IEEE Computer, 2007
Peng et. al, “Traffic-Driven Power Savings in Operational 3G Cellular Networks”, MOBICOM 2011
Workload
Power consumption (Watt)
Google: Search queries
Diurnal cycles

## Slide 8
When workload rises even more …
Key Idea
TX
CA
Electricity price
$/MWh
Workload relocation (WR)
Least expensive
Workload relocation cuts electricity cost further
Resource pruning cuts electricity cost
NY
Data Center
52
72
122.4
Most expensive
As workload rises…
Deactivate idle equipment
Deactivate some equipment
Workload
CA: California
NY: New York
TX: Texas
Move workload from NY to TX
RP to save more
RP and WR can cut electricity costs
Ain’t no such thing as a free lunch
A. Qureshi et. al, “Plugging into energy market diversity”, HOTNETS 2008
Geographic diversity in electricity prices
Temporal diversity in electricity prices
Notes: Bigger. Photo of a real data center then zoom

## Slide 9: Transition Costs
Workload relocation overheads
  E.g., Cost of data transfers
    Expensive inter-data center links
Equipment activation and de-activation overheads
  E.g., Energy spent while resuming and sleeping
Must consider transition costs while optimizing
Relocate Energy Demand to Better Locations (RED-BL)

## Slide 10: This Thesis
Towards systematic minimization of network electricity cost
using Workload Relocation (WR) and Resource Pruning (RP)
while considering transition costs
Notes: Abbreviate. Single thesis statement
This thesis uses (boxes) WR and RP with consideration of relocation and (transition) costs by developing a systematic framework for electricity cost minimization

## Slide 11: Contributions
Optimal state trajectory formulation [1]
Considered transition costs [1]
Evaluation of cost savings under various scenarios using real traces [1]
Evaluated impact of prediction accuracy on savings [1]
[1] “RED-BL: Energy Solution for Loading Data Centers”, Infocom 2013 mini-conference

## Slide 12: Contributions
Evaluation of RED-BL with:
  Partial data center shutdown [2]
  Sleep modes [2]
Sliding window re-optimization [2]
Granular deactivation of data center equipment [2]
Showed that RED-BL (for data centers) is the NP-Complete unit commit problem [2]
[2] “RED-BL: Evaluating Dynamic Right Sizing for Data Center Networks”, Elsevier Computer Networks, 2014

## Slide 13: Contributions
Application of state trajectory optimization to cellular networks [2, 3]
Showed that RED-BL for cellular networks is NP-Hard [4]
Evaluated RED-BL using traces from a live network [3, 4]
[3] “Electricity Cost Efficient Workload Mapping”, IEEE INFOCOM 2013 Computer Communications Workshop
[4] “Low-Carb: Reducing Energy Consumption in Operational Cellular Networks” IEEE GLOBECOM 2013

## Slide 14: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers (e.g., Facebook and Google)
  Cellular networks (e.g., Sprint and Verizon)
Conclusions and future work

## Slide 15: Case Study – I : Background
Data center operator
  Geographically distributed data centers
Data center equipment
Power drawn is affine function of workload
IT Load | Non-IT Load
Servers | Lighting
Storage | Cooling
Network | Power distribution
Source: http://bit.ly/1mrIi7o
Let’s recap how we can use WR and RP
Notes: Photo

## Slide 16: Problem Model
TX
NY
TX
NY
CA
TX
Interval - 1
Interval - 2
Interval - 3
CA
CA
NY
Network State
12
10
10
State Cost
Data center activation
Data center deactivation
8
6
Transition cost
Optimal State Trajectory Problem
Might not be globally optimal
TX
NY
CA
NY
CA
NY
14
12
12
4
0
CA
TX
TX
State cost locally suboptimal
Relocate Energy Demand to Better Locations (RED-BL)
Total cost: 42
Total cost: 46
Electricity price driven workload assignment
Sum of all data centers’ electricity cost
Locally optimal
An alternative workload mapping
State cost locally suboptimal
Transition costs lower than local optimal scheme
State cost locally suboptimal
No transition costs

## Slide 17: Optimization Formulation
Sum over all intervals
Sum over all data centers
Subject to several constraints (please see the thesis)
Transition energy
State energy
Workload
Data center capacity
Fraction of data center that is active
Unit price of electricity
Notes: Give the objective function and the constraints

## Slide 18: Experimental Setup
Workload from 3 popular Facebook apps
Electricity prices from 33 US locations
Simulated a week-long deployment plan
Compared RED-BL against various schemes
Notes: To evaluate RED-BL for geo-diverse data centers, we performed a simulation study which had the following setup. We used workload from three popular Facebook applications and normalized the cumulative workload. We verified that the characteristics of the cumulative workload resemble that of the workload for thousands of servers in a Google data center. We collected day-ahead electricity prices for 33 locations across the USA and simulated a weeklong deployment plan for the data centers situated at these locations. We compared RED-BL against a number of algorithms.

## Slide 19: Comparison Benchmarks
LO: Local Optimal Ignoring Transition Costs
LD: Local Optimal with Deactivation
LS: Local Optimal with Selection
UNIFORM: Equally distribute workload
3
3
1
15
15
20
0
0
2
2
2
1
1
3
2
1
2
1
3
2
3
3
1
12
10
10
8
6
2
1
2
1
3
2
3
3
1
15
10
10
4
6
2
1
2
1
3
2
3
3
1
12
10
10
0
0
Theoretical lower bound
Sometimes idling is better
Best practical variant of local optimal

## Slide 20: Cost Savings vs Over-provisioning
RED-BL close to ideal savings
Falsely predicts high savings
Actual savings 10.35% lower
50% over provisioning => 26% Savings

## Slide 21: Electricity Cost vs Transition Cost
(De)activation overhead = energy cost
No transition costs
Near optimal savings
Gap widens rapidly
Notes: As the magnitude of transition overheads compared to the cost of handling workload increases, we see that the percentage savings in electricity cost decrease for all algorithms. RED-BL achieves close to the ideal lower bound electricity cost savings, whereas the best variants of the greedy algorithm scale worse than RED-BL.

## Slide 22: Granular (De)activation
Can only (de)activate entire data center
Can (de)activate half a data center
Cost savings over full data center (de)activation
Opportunity for greater savings
Notes: Now, let’s see how RED-BL energy savings would improve if we allowed independent (de)activation of fixed size fractions of a data center. The extreme right handside of this graph represents the case where you can only (de)activate an entire data center at a time. This is 0% better than the standard “all or nothing” RED-BL, because it is the same thing. If we were able to (de)activate half a data center at a time, we could do about 2.5% better than standard RED-BL. If we were able to independently (de)activate 10% of a data center at a time, we could do 5% better than standard RED-BL. So, there is opportunity for greater savings with granular (de)activation and it has a linear trend.

## Slide 23: DVFS Instead of Deactivation
Notes: If, instead of shutting down an entire data center, we switch the servers into lower-power mode using DVFS techniques, the power savings might reduce, but the scheme would be more agile to workload variations. Here, we see that the power consumption drops linear as the power consumption is lowered with DVFS. If the server power consumption drops to 10% of the peak, the data center power consumption would be reduced by about 70%. Another data point is that if we put all “idle” servers at 50% power consumption, we achieve about 20% power reduction.

## Slide 24: Reserve Margin
Notes: To be prepared for some stray workload at data centers which we planned to deactivate, we’ll keep some servers on as reserve. As we increase the amount of serving capacity in reserve mode, the difference in power consumption will increase compared to the scenario where we did not keep any reserve capacity.
Exactly how much “stray” traffic we receive can’t be predicted. In this chart, the lower line shows the situation where we don’t receive any stray traffic at all. The power consumption in that case is purely due to servers idling. The upper line represents the situation where we need all the reserve capacity for handling stray traffic. The actual situation may be somewhere in between.

## Slide 25: Summary – Case Study I
Significant cost savings are possible using RED-BL
Finer granularity of resource (de)activation increases savings
Low-power mode instead of shutdown also helps considerably
Cost savings decrease sharply with reserve margin
Can we apply this optimization “machinery” to other networks?

## Slide 26: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers (e.g., Facebook and Google)
  Cellular networks (e.g., Sprint and Verizon)
Conclusions and future work

## Slide 27: Case Study II Cellular Networks
BSC
BSC
MSC
15%-80% of total power consumption
TRXs
Power amplifiers
Air conditioning
Notes: Give the motivating example to show that WR and RP can be used in cellular networks as well.

## Slide 28: Resource Pruning
Call volume
BTS Power Consumption (kW)
Power saving threshold (d)
Pmax
Pmin
Workload capacity
d
tmax
Low call volume => Deactivate some TRXs
No. of calls ≤ d

## Slide 29: Does workload relocation help?
Assume that power saving is enabled if upto two calls are being served
Power saving
Power saving
Power saving
Handing off some calls may enable greater power savings

## Slide 30: Is Workload Relocation Possible?

## Slide 31: Drawing Parallels With Case Study I
Parameter | Cellular network | Data centers
Network resource
Workload relocation
Resource pruning
Transition costs
TRX
Call hand off
Negligible
Servers
Client redirect
Server shutdown / idle / hibernate
(De)activation overheads
BTS Power Saving
Notes: Identify the similarities and differences between the two networks and observe how abstractions can be made.

## Slide 32: Optimization Formulation
For every interval, minimize # TRXs
Seemingly simple formulation
NP-Hard

## Slide 33: Complexity 1/2
RED-BL: Minimum cardinality subset that covers J
Call this graph problem:
Modified MDS
(d + 1)th call incurs a sudden jump in power
Other calls bring a small increase in power (e)
Set J
(Calls)
Set K
(BTSs)
Call volume
BTS Power Consumption (kW)
d
tmax
d
Set d = 0
At every BTS
First call incurs a sudden jump in power (g)
Optimal solution will use fewest possible BTSs
BTS Cost:
0 calls: 0
n calls: g + ne

## Slide 34: Complexity 2/2
A
B
C
D
Minimum Dominating Set (MDS)
Smallest subset V’ of vertices V such that every other vertex is adjacent to at least one vertex in V’
A
B
C
D
A’
B’
C’
D’
Make two copies of vertices
Place edges between each vertex and its copy
Replicate other edges in original graph
Solve Modified MDS on new graph
Set J
(Calls)
Set K
(BTSs)
MDS Solved!
RED-BL for cellular
solves
Modified MDS
MDS
solves
NP-Hard
NP-Hard

## Slide 35: Experimental Setup
Call volume traces for 2 days at 26 urban BTSs
Trace driven simulation:
  Periodically obtain optimal call placement
  Place BTSs with low-traffic in power-saving mode

## Slide 36: BTS Power Consumption Models
Parameter | Value |  | 
 | Model 1 | Model 2 | Model 3
Idle Power (W) | 1425 | 2401.8 | 2341.5
Peak Power (W) | 1500 | 3887.5 | 2973.9
Power Saving per TRX (W) | 20 | 50 | 100

## Slide 37: Results: Power-Saving Feature Only
Energy savings | Model 1 | Model 2 | Model 3
Percentage | 4.73% | 5.43% | 12.89%
Daily energy savings (kWh) | 43.28 | 109.68 | 217.12
Country-wide daily savings -31000 sites (MWh) | 51.6 | 130.77 | 258.87

## Slide 38: Results: Power-Saving + Handoff Absolute Energy Savings (%)

## Slide 39: Results: Power-Saving + Handoff Absolute Energy Savings (kWh)

## Slide 40: Effect of Granular Deactivation
Granularity | Model 1 | Model 2 | Model 3
2-state | 5.38% | 6.29% | 14.94%
3-state | 6.81% | 7.73% | 18.62%
6-state | 8.70% | 9.65% | 23.37%
Savings increase with finer granularity

## Slide 41: Effect of Late Deactivation

## Slide 42: A Randomized Algorithm
Pick this
While there are BTSs in high-power mode
  Pick a random BTS
  For each call being handled by this BTS
    Hand-over to a candidate BTS in low-power mode
Nope
Nope
Yup!
Power saving
Power saving

## Slide 43: Performance of Heuristic Algorithm

## Slide 44: Case Study II - Summary
Traffic has limited geo-flexibility compared to data centers
No geo-diversity in electricity prices
Activation of power savings feature in hardware helps
RED-BL achieves greater savings even for relatively conservative settings

## Slide 45: Agenda
Background and motivation
Opportunity and key idea
Case studies:
  Data centers (e.g., Facebook and Google)
  Cellular networks (e.g., Sprint and Verizon)
Conclusions and future work

## Slide 46: Conclusions
Opportunities for electricity cost savings using:
  Workload relocation
  Resource pruning
WR and RP are applicable to:
  Data centers
  Cellular networks
  Others (need to explore)

## Slide 47: Conclusions
Modeled electricity cost minimization as an optimal state trajectory problem
Showed the problem to be NP-Hard in the two case studies
Studied the sensitivity of the problem to various parameters

## Slide 48: Conclusions
Data centers and cellular networks:
  Sets of geo-diverse resources
Contrasts:
  Availability of geo-diversity in electricity prices
  Geo-flexibility in traffic
  Magnitude of transition costs

## Slide 49: Future Work
Factor in other forms of transition costs:
  Cost of change in latency
  Cost of replication
  Cost of increase in call blocking probability
Implementation on software BTS
Incorporation into an OA&M framework
Adaptation to recent generations of cellular networks
Consider expensive diesel-generated power in cellular BTSs

## Slide 50: Questions and Answers
If you can read this
Murphy’s law was violated

## Slide 51: List of Papers
Published:
  A simulation study of GELS for Ethernet over WAN, GLOBECOM 2007
  RED-BL: Energy solution for loading data centers, INFOCOM Mini-Conference, 2012
  Electricity cost efficient workload mapping, INFOCOM Computer Communications Workshop, 2013
  Low-Carb: Reducing energy consumption in operational cellular networks, GLOBECOM 2013
  RED-BL: Evaluating dynamic right sizing for data centers, Computer Networks, vol. 72, 2014
Submitted:
  Low-Carb: A practical scheme for improving energy efficiency in cellular networks

## Slide 52: Questions 1
Why not have one data center at the cheapest locations?
  There is no single cheapest location
  Diversity for:
    Disaster
    Latency

## Slide 53: Question 2
Why can’t DVFS be used?
  It can certainly be used
  It does not achieve fine grained energy proportionality
    Granularity of VF scaling is coarse
    Other components are also energy proportional

## Slide 54: Question 3
How many transitions in a day are likely?

## Slide 55: Question 4
How quick is a transition?