## Slide 1: Cutting Electricity Cost For Service Provider Networks
Muhammad Saqib Ilyas

## Slide 2: Agenda
Background and motivation
Problem statement and formulation
Two case studies – simulation results
Conclusions and future work

## Slide 3: Motivation
Large scale networks:
  Enable critical services
  Consume a lot of energy
A 100 MW data center in the US ~ $114 M/year
Network electricity costs expected to increase
  Electricity prices are rising globally

## Slide 4: Example – Google Search
Data center
User
Traffic is distributed amongst data centers
Arriving traffic is data center workload
1
2
3
How does this relate to data center power consumption?

## Slide 6
TODO
General description of benefits of geo-diversity and pruning
Identify presence of opportunities

## Slide 7: Using Cheaper Electricity
Data Centers
2
3
Electricity price
Workload relocation (WR)
Workload
Data Center 2 least expensive
As workload rises…
Significant idling power
Workload relocation can help reduce electricity cost
Resource pruning (RP)
Resource pruning can help further reduce electricity cost
1
Relocate Energy Demand to Cheaper Locations (RED-CL)
Workload
Real
Ideal
Power consumption (Watt)
When workload rises even more …
Data Center
Data Center 3 most expensive

## Slide 8: This Thesis
Cut network electricity costs by:
  Using cheaper electricity
    Workload Relocation (WR)
  Reducing idling power consumption
    Resource Pruning (RP)
TODO: Generic cost reduction techniques
  application to other networks
We investigated:
  Data Centers
  Cellular networks

## Slide 9: Case Study I – Data Centers
2
1
2
1
3
2
Electricity Price
Interval - 1
Interval - 2
Interval - 3
3
3
1
Network State
12
10
10
State Cost
Data center activation
Data center deactivation
8
6
Transition cost
Optimal State Trajectory Problem
RED-CL might not be optimal
2
1
3
1
3
1
14
12
12
4
0
3
2
2
State cost higher than RED-CL
State cost higher than RED-CL
State cost higher than RED-CL
Relocate Energy Demand to Better Locations (RED-BL)
Total cost: 42
Total cost: 46
Transition costs lower than RED-CL

## Slide 10: Optimization Formulation
Sum over all intervals
Sum over all data centers
Subject to several constraints (please see the thesis)
Transition energy
State energy
Workload
Data center capacity
Fraction of data center that is active
Unit price of electricity
Notes: Give the objective function and the constraints

## Slide 11: Experimental Setup
Workload from 3 popular Facebook apps
Electricity prices from 33 US locations
Simulated a week-long deployment plan
Compared RED-BL against various algorithms
Notes: To evaluate RED-BL for geo-diverse data centers, we performed a simulation study which had the following setup. We used workload from three popular Facebook applications and normalized the cumulative workload. We verified that the characteristics of the cumulative workload resemble that of the workload for thousands of servers in a Google data center. We collected day-ahead electricity prices for 33 locations across the USA and simulated a weeklong deployment plan for the data centers situated at these locations. We compared RED-BL against a number of algorithms.

## Slide 12: Comparison Benchmarks
LI: Local Optimal with Idling
LO: LI ignoring transition costs
LD: Local Optimal with Deactivation
LS: Local Optimal with Selection
UNIFORM: Equally distribute workload
2
1
2
1
3
2
3
3
1
20
18
18
0
0
2
1
2
1
3
2
3
3
1
12
10
10
0
0
3
3
1
15
15
20
0
0
2
2
2
1
1
3
2
1
2
1
3
2
3
3
1
12
10
10
8
6
2
1
2
1
3
2
3
3
1
15
10
10
4
6

## Slide 13: Cost Savings vs Over-provisioning
RED-BL close to ideal savings
Falsely predicts high savings
Actual savings 10.35% lower
50% over provisioning => 26% Savings

## Slide 14: Electricity Cost vs Transition Cost
(De)activation overhead = energy cost
No transition costs
Near optimal savings
Gap widens rapidly
Notes: As the magnitude of transition overheads compared to the cost of handling workload increases, we see that the percentage savings in electricity cost decrease for all algorithms. RED-BL achieves close to the ideal lower bound electricity cost savings, whereas the best variants of the greedy algorithm scale worse than RED-BL.

## Slide 15: Granular (De)activation
Can only (de)activate entire data center
Can (de)activate half a data center
Cost savings over full data center (de)activation
Opportunity for greater savings
Notes: Now, let’s see how RED-BL energy savings would improve if we allowed independent (de)activation of fixed size fractions of a data center. The extreme right handside of this graph represents the case where you can only (de)activate an entire data center at a time. This is 0% better than the standard “all or nothing” RED-BL, because it is the same thing. If we were able to (de)activate half a data center at a time, we could do about 2.5% better than standard RED-BL. If we were able to independently (de)activate 10% of a data center at a time, we could do 5% better than standard RED-BL. So, there is opportunity for greater savings with granular (de)activation and it has a linear trend.

## Slide 16: DVFS Instead of Deactivation
Notes: If, instead of shutting down an entire data center, we switch the servers into lower-power mode using DVFS techniques, the power savings might reduce, but the scheme would be more agile to workload variations. Here, we see that the power consumption drops linear as the power consumption is lowered with DVFS. If the server power consumption drops to 10% of the peak, the data center power consumption would be reduced by about 70%. Another data point is that if we put all “idle” servers at 50% power consumption, we achieve about 20% power reduction.

## Slide 17: Reserve Margin
Notes: To be prepared for some stray workload at data centers which we planned to deactivate, we’ll keep some servers on as reserve. As we increase the amount of serving capacity in reserve mode, the difference in power consumption will increase compared to the scenario where we did not keep any reserve capacity.
Exactly how much “stray” traffic we receive can’t be predicted. In this chart, the lower line shows the situation where we don’t receive any stray traffic at all. The power consumption in that case is purely due to servers idling. The upper line represents the situation where we need all the reserve capacity for handling stray traffic. The actual situation may be somewhere in between.

## Slide 18: Summary – Case Study I
Significant cost savings are possible using RED-BL
Finer granularity of resource (de)activation increases savings
Low-power mode instead of shutdown also helps considerably
Cost savings decrease sharply with reserve margin
Can we apply this optimization “machinery” to other networks?

## Slide 19: Case Study II Cellular Networks
BSC
BSC
MSC
15%-80% of total power consumption
TRXs
Power amplifiers
Air conditioning
Built-in power saving mode (RP)
Notes: Give the motivating example to show that WR and RP can be used in cellular networks as well.

## Slide 20: Does workload relocation help?
Assume that power saving is enabled if upto two calls are being served
Power saving
Power saving
Power saving
Handing off some calls may enable greater power savings

## Slide 21: Is Workload Relocation Possible?

## Slide 22: Drawing Parallels With Case Study I
Parameter | Cellular network | Data centers
Network resource
Workload relocation
Resource pruning
Transition costs
TRX
Call hand off
Negligible
Servers
Client redirect
Server shutdown / idle / hibernate
(De)activation overheads
BTS Power Saving
Notes: Identify the similarities and differences between the two networks and observe how abstractions can be made.

## Slide 23: Optimization Formulation
(De)activation overheads negligible
Contributes a constant
Electricity price diversity may be ignored
Constant
Constant
Constant
Assume homogeneity

## Slide 24: Complexity
Objective: Minimum number of active TRXs
Callers
BTSs

## Slide 25: Experimental Setup
Call volume traces for 2 days at 26 urban BTSs
Trace driven simulation:
  Periodically obtain optimal call placement
  Place BTSs with low-traffic in power-saving mode

## Slide 26: BTS Power Consumption Models
Parameter | Value |  | 
 | Model 1 | Model 2 | Model 3
Idle Power (W) | 1425 | 2401.8 | 2341.5
Peak Power (W) | 1500 | 3887.5 | 2973.9
Power Saving per TRX (W) | 20 | 50 | 100

## Slide 27: Results: Power-Saving Feature Only
Energy savings | Model 1 | Model 2 | Model 3
Percentage | 4.73% | 5.43% | 12.89%
Daily energy savings (kWh) | 43.28 | 109.68 | 217.12
Country-wide daily savings -31000 sites (MWh) | 51.6 | 130.77 | 258.87

## Slide 28: Results: Power-Saving + Handoff Absolute Energy Savings (%)

## Slide 29: Results: Power-Saving + Handoff Absolute Energy Savings (kWh)

## Slide 30: Effect of Granular Deactivation
Granularity | Model 1 | Model 2 | Model 3
2-state | 5.38% | 6.29% | 14.94%
3-state | 6.81% | 7.73% | 18.62%
6-state | 8.70% | 9.65% | 23.37%

## Slide 31: A Randomized Algorithm
Pick this
While there are BTSs in high-power mode
  Pick a random BTS
  For each call being handled by this BTS
    Hand-over to a candidate BTS in low-power mode
Nope
Nope
Yup!
Power saving
Power saving

## Slide 32: Performance of Heuristic Algorithm

## Slide 33: Effect of Late Deactivation

## Slide 34: Case Study II - Summary
Traffic has limited geo-flexibility compared to data centers
No geo-diversity in electricity prices
Mere activation of power savings feature supported in hardware helps
RED-BL achieves greater savings even for relatively conservative settings

## Slide 35: Conclusions
Abstracted data centers and cellular networks
Similarity:
  May be modeled as sets of geo-diverse resources
Contrasts:
  Availability of geo-diversity in electricity prices
  Geo-flexibility in traffic
  Magnitude of transition costs

## Slide 36: Conclusions
Mapping of workload to resources => Network state
Network state has bearing on electricity cost
Model electricity cost minimization as an optimal state trajectory problem
Showed the problem to be NP-Complete in the two case studies
Studied the sensitivity of the problem to various parameters

## Slide 37: Future Work
Factor in other forms of transition costs:
  Cost of change in latency
  Cost of replication
  Cost of increase in call blocking probability
Implementation on software BTS
Adaptation to recent generations of cellular networks
Consider expensive diesel-generated power in cellular BTSs

## Slide 38: Questions and Answers

## Slide 39: List of Papers
Published:
  A simulation study of GELS for Ethernet over WAN, GLOBECOM 2007
  RED-BL: Energy solution for loading data centers, INFOCOM Mini-Conference, 2012
  Electricity cost efficient workload mapping, INFOCOM Computer Communications Workshop, 2013
  Low-Carb: Reducing energy consumption in operational cellular networks, GLOBECOM 2013
  RED-BL: Evaluating dynamic right sizing for data centers, Computer Networks, vol. 72, 2014
Submitted:
  Low-Carb: A practical scheme for improving energy efficiency in cellular networks