## Slide 1: Cutting Electricity Cost For Service Provider Networks
Muhammad Saqib Ilyas

## Slide 2: Agenda
Background and motivation
Problem statement and formulation
Two case studies
Conclusions and future work

## Slide 3: Background
Image source: darciec.com
Brought to you by…
Notes: Change background details

## Slide 4: Motivation
$951 M
Source: datacenterknowledge.com
$143 M
Source: Greenberg et. al, CCR 2009
Chart: 
| Others | Electricity Bill
 | 85 | 15
Electricity Bill
15%
Annual DC Opex
Electricity Cost
Chart: 
 | 82 | 18
Chart: 
 | 50 | 50
Electricity Bill
18%
Electricity Bill
50%
$81 M
Electricity Cost 2012
Source: GREENNETS
Significant electricity costs

## Slide 5: Example – Google Search
Data center
User
Traffic is distributed amongst data centers
Arriving traffic is data center workload
1
2
3
How does this relate to data center electricity cost?
Electricity Price Diversity
$0.32
$0.13
$0.25
Where would you like to consume the most energy?
Sure. But, how?

## Slide 6: Data Center Energy Consumption
Energy: Accumulation of power consumption
Consume power where electricity is cheaper
Data center power consumption depends on:
  Its workload capacity
  Workload assigned to it
Fixed
Controllable

## Slide 7: Example – Google Search
1
2
3
$0.32
$0.13
$0.25
Workload: 0
Workload: 0
Power consumption also 0?
Power consumption also 0?
Workload Relocation (WR): Cuts electricity costs

## Slide 8: High Idling Power
Data centers are not energy proportional
  Idle power 75%-85% of peak
  Because even idling equipment consumes power
Opportunity:
  Deactivate idle equipment to cut power
Source: Emerson, “Energy Logic: Reducing Data Center Power Consumption…”

## Slide 9: High Idling Power: A remedy
1
2
3
$0.32
$0.13
$0.25
Workload: 0
Workload: 0
Deactivate some equipment
Deactivate some equipment
Resource Pruning (RP): Cuts electricity costs even further

## Slide 10: This Thesis
Cut network electricity costs by:
  Using cheaper electricity
    Workload Relocation (WR)
  Reducing idling power consumption
    Resource Pruning (RP)
Towards a generic framework for electricity cost reduction
Possible application to different networks
  We investigated:
    Data Centers
    Cellular networks

## Slide 11: Case Study – I : Background
Data center operator
  Geographically distributed data centers
Data center equipment
Workload handled by servers
  Causes power consumption
IT Load | Non-IT Load
Servers | Lighting
Storage | Cooling
Network | Power distribution

## Slide 12: Case Study – I : Background
Workload
Real
Ideal
Power consumption (Watt)
Workload => Power
Energy
x Electricity Price
=>
Electricity Cost =

## Slide 13: Problem Model
1
2
3
Data Centers
Electricity price
Data Center 2 least expensive
Consume most energy at cheapest location
Time
Workload
Data Center 3 most expensive
Relocate Energy Demand to Cheaper Locations (RED-CL)

## Slide 14: Problem Model
2
1
2
1
3
2
Electricity Price
Interval - 1
Interval - 2
Interval - 3
3
3
1
Network State
12
10
10
State Cost
Data center activation
Data center deactivation
8
6
Transition cost
Optimal State Trajectory Problem
RED-CL might not be optimal
2
1
3
1
3
1
14
12
12
4
0
3
2
2
State cost higher than RED-CL
State cost higher than RED-CL
State cost higher than RED-CL
Relocate Energy Demand to Better Locations (RED-BL)
Total cost: 42
Total cost: 46
Transition costs lower than RED-CL

## Slide 15: Optimization Formulation
Sum over all intervals
Sum over all data centers
Subject to several constraints (please see the thesis)
Transition energy
State energy
Workload
Data center capacity
Fraction of data center that is active
Unit price of electricity
Notes: Give the objective function and the constraints

## Slide 16: Experimental Setup
Workload from 3 popular Facebook apps
Electricity prices from 33 US locations
Simulated a week-long deployment plan
Compared RED-BL against various algorithms
Notes: To evaluate RED-BL for geo-diverse data centers, we performed a simulation study which had the following setup. We used workload from three popular Facebook applications and normalized the cumulative workload. We verified that the characteristics of the cumulative workload resemble that of the workload for thousands of servers in a Google data center. We collected day-ahead electricity prices for 33 locations across the USA and simulated a weeklong deployment plan for the data centers situated at these locations. We compared RED-BL against a number of algorithms.

## Slide 17: Comparison Benchmarks
LI: Local Optimal with Idling
LD: Local Optimal with Deactivation
LS: Local Optimal with Selection
UNIFORM: Equally distribute workload
2
1
2
1
3
2
3
3
1
20
18
18
0
0
3
3
1
15
15
20
0
0
2
2
2
1
1
3
2
1
2
1
3
2
3
3
1
12
10
10
8
6
2
1
2
1
3
2
3
3
1
15
10
10
4
6

## Slide 18: Cost Savings vs Over-provisioning
RED-BL close to ideal savings
Falsely predicts high savings
Actual savings 10.35% lower
50% over provisioning => 26% Savings

## Slide 19: Electricity Cost vs Transition Cost
(De)activation overhead = energy cost
No transition costs
Near optimal savings
Gap widens rapidly
Notes: As the magnitude of transition overheads compared to the cost of handling workload increases, we see that the percentage savings in electricity cost decrease for all algorithms. RED-BL achieves close to the ideal lower bound electricity cost savings, whereas the best variants of the greedy algorithm scale worse than RED-BL.

## Slide 20: Granular (De)activation
Can only (de)activate entire data center
Can (de)activate half a data center
Cost savings over full data center (de)activation
Opportunity for greater savings
Notes: Now, let’s see how RED-BL energy savings would improve if we allowed independent (de)activation of fixed size fractions of a data center. The extreme right handside of this graph represents the case where you can only (de)activate an entire data center at a time. This is 0% better than the standard “all or nothing” RED-BL, because it is the same thing. If we were able to (de)activate half a data center at a time, we could do about 2.5% better than standard RED-BL. If we were able to independently (de)activate 10% of a data center at a time, we could do 5% better than standard RED-BL. So, there is opportunity for greater savings with granular (de)activation and it has a linear trend.

## Slide 21: DVFS Instead of Deactivation
Notes: If, instead of shutting down an entire data center, we switch the servers into lower-power mode using DVFS techniques, the power savings might reduce, but the scheme would be more agile to workload variations. Here, we see that the power consumption drops linear as the power consumption is lowered with DVFS. If the server power consumption drops to 10% of the peak, the data center power consumption would be reduced by about 70%. Another data point is that if we put all “idle” servers at 50% power consumption, we achieve about 20% power reduction.

## Slide 22: Reserve Margin
Notes: To be prepared for some stray workload at data centers which we planned to deactivate, we’ll keep some servers on as reserve. As we increase the amount of serving capacity in reserve mode, the difference in power consumption will increase compared to the scenario where we did not keep any reserve capacity.
Exactly how much “stray” traffic we receive can’t be predicted. In this chart, the lower line shows the situation where we don’t receive any stray traffic at all. The power consumption in that case is purely due to servers idling. The upper line represents the situation where we need all the reserve capacity for handling stray traffic. The actual situation may be somewhere in between.

## Slide 23: Summary – Case Study I
Significant cost savings are possible using RED-BL
Finer granularity of resource (de)activation increases savings
Low-power mode instead of shutdown also helps considerably
Cost savings decrease sharply with reserve margin
Can we apply this optimization “machinery” to other networks?

## Slide 24: Case Study II Cellular Networks
BSC
BSC
MSC
15%-80% of total power consumption
TRXs
Power amplifiers
Air conditioning
Built-in, optional power saving mode => RP
Notes: Give the motivating example to show that WR and RP can be used in cellular networks as well.

## Slide 25: Power Consumption Model and RP
Power consumption (Watt)
Number of calls
If traffic < 50%,
deactivate half TRXs
Great! RP Works
But, what about WR?

## Slide 26: Does workload relocation help?
Assume that power saving is enabled if upto two calls are being served
Power saving
Power saving
Power saving
Handing off some calls may enable greater power savings

## Slide 27: Is Workload Relocation Possible?

## Slide 28: Drawing Parallels With Case Study I
Parameter | Cellular network | Data centers
Network resource
Workload relocation
Resource pruning
Transition costs
TRX
Call hand off
Negligible
Servers
Client redirect
Server shutdown / idle / hibernate
(De)activation overheads
BTS Power Saving
Notes: Identify the similarities and differences between the two networks and observe how abstractions can be made.

## Slide 29: Optimization Formulation
For every interval, minimize # TRXs
Simple optimization formulation
NP-Hard

## Slide 30: Complexity
Modified Dominating Set
Callers
BTSs
J
K
Minimum cardinality subset that covers J

## Slide 31: Experimental Setup
Call volume traces for 2 days at 26 urban BTSs
Trace driven simulation:
  Periodically obtain optimal call placement
  Place BTSs with low-traffic in power-saving mode

## Slide 32: BTS Power Consumption Models
Parameter | Value |  | 
 | Model 1 | Model 2 | Model 3
Idle Power (W) | 1425 | 2401.8 | 2341.5
Peak Power (W) | 1500 | 3887.5 | 2973.9
Power Saving per TRX (W) | 20 | 50 | 100

## Slide 33: Results: Power-Saving Feature Only
Energy savings | Model 1 | Model 2 | Model 3
Percentage | 4.73% | 5.43% | 12.89%
Daily energy savings (kWh) | 43.28 | 109.68 | 217.12
Country-wide daily savings -31000 sites (MWh) | 51.6 | 130.77 | 258.87

## Slide 34: Results: Power-Saving + Handoff Absolute Energy Savings (%)

## Slide 35: Results: Power-Saving + Handoff Absolute Energy Savings (kWh)

## Slide 36: Effect of Granular Deactivation
Granularity | Model 1 | Model 2 | Model 3
2-state | 5.38% | 6.29% | 14.94%
3-state | 6.81% | 7.73% | 18.62%
6-state | 8.70% | 9.65% | 23.37%

## Slide 37: A Randomized Algorithm
Pick this
While there are BTSs in high-power mode
  Pick a random BTS
  For each call being handled by this BTS
    Hand-over to a candidate BTS in low-power mode
Nope
Nope
Yup!
Power saving
Power saving

## Slide 38: Performance of Heuristic Algorithm

## Slide 39: Effect of Late Deactivation

## Slide 40: Case Study II - Summary
Traffic has limited geo-flexibility compared to data centers
No geo-diversity in electricity prices
Mere activation of power savings feature supported in hardware helps
RED-BL achieves greater savings even for relatively conservative settings

## Slide 41: Conclusions
Abstracted data centers and cellular networks
Similarity:
  May be modeled as sets of geo-diverse resources
Contrasts:
  Availability of geo-diversity in electricity prices
  Geo-flexibility in traffic
  Magnitude of transition costs

## Slide 42: Conclusions
Mapping of workload to resources => Network state
Network state has bearing on electricity cost
Model electricity cost minimization as an optimal state trajectory problem
Showed the problem to be NP-Complete in the two case studies
Studied the sensitivity of the problem to various parameters

## Slide 43: Future Work
Factor in other forms of transition costs:
  Cost of change in latency
  Cost of replication
  Cost of increase in call blocking probability
Implementation on software BTS
Adaptation to recent generations of cellular networks
Consider expensive diesel-generated power in cellular BTSs

## Slide 44: Questions and Answers

## Slide 45: List of Papers
Published:
  A simulation study of GELS for Ethernet over WAN, GLOBECOM 2007
  RED-BL: Energy solution for loading data centers, INFOCOM Mini-Conference, 2012
  Electricity cost efficient workload mapping, INFOCOM Computer Communications Workshop, 2013
  Low-Carb: Reducing energy consumption in operational cellular networks, GLOBECOM 2013
  RED-BL: Evaluating dynamic right sizing for data centers, Computer Networks, vol. 72, 2014
Submitted:
  Low-Carb: A practical scheme for improving energy efficiency in cellular networks