## Slide 1: RED-BL

## Slide 2: Overview
Background and motivation
Problem statement and formulation
Case studies
Conclusion

## Slide 3: Introduction
Notes: Today, we use many different applications every day to communicate with friends and family, for entertainment and shopping etc. These services are enabled by different types of networks. We’ve got Internet Service Providers that provide connectivity to the Internet. We’ve got Cellular Network Operators that provide cellular telephony and data services. But there are other networks behind the scenes, too. For instance, web applications are hosted in large geo-distributed data centers run by data center operators like Amazon, Microsoft, Google and Facebook. Then, there are companies that replicate content across the globe with the objective of reducing client latency, such as Akamai, Edgecast and Internap. The bottom line is that different types of networks enable services that are critical to our personal and professional lives. One commonality amongst all these networks is that they are really expensive to deploy and maintain. In this thesis, we focus on cellular networks and geo-diverse data center networks.

## Slide 4: The Cost of a Network
$ 550,000
$ 400 Million
Capital cost
Operations cost
[TechCrunch]
FB (2008) > $1 M
Telecom Italia (2012): $81 M
[Greenberg et. Al, CCR 2009] 15%
[GREENNETS]
18 - 50% in EU
Notes: Especially when it comes to services on the Internet, we are used to a plethora of free services like web based email and online social networking, but deploying and running the networks that enable these services costs a significant amount of money. According to a study conducted in 2010, a typical cell site can cost as much as $ 550,000. In 2013, Google announced building a data center in Iowa at a cost of $400 Million. But that’s just the capital cost of establishing the network infrastructure. The recurring operations cost is significant, too.
Facebook spent about $50 Million dollar in space leases whereas

## Slide 5: Network Structure
BSC
BSC
MSC
…
…
…
…
The Internet
…
Notes: Let’s see what a cellular network consists of. Of course, there are end user devices called mobile stations. These devices connect to the cellular network through cell sites also termed as BTSs. A BTSs job is radio signal transmission and reception. Several BTSs in geographic proximity are coordinated and controlled by a BSC. The BSC assigns radio frequencies to the BTSs. Several BSCs are interconnected through MSCs, which do call routing. It turns out that most of the power consumption in a cellular network takes place at BTSs. So, let’s dig deeper into the BTSs.

## Slide 6: Some Similarities
…
Workload
Geo-distributed
network sites
Network
resources
Workload
capacity
Power
consumption
Notes: If we look carefully at routine network operation, there are several similarities, and of course some differences between these networks. Let’s focus on geo-diverse data centers and cellular networks. The first similarity is that they both have customer workload, e.g., customer calls in cellular networks and web site page visits in case of data center networks. Another similarity is that both of these networks have geographically distributed network sites, such as data centers and base transceiver stations or BTS for short. Then, there is some sort of workload mapping function that directs customer workload to one of the network sites. Each network site consists of a number of network resources such as radio transceivers in case of cellular networks and servers, storage etc., in case of data centers. Yet another similarity is that as you increase the number of deployed resources, the workload handling capacity increases as does the power consumption.
In cellular networks, user traffic needs to be handled. Data centers also handle user traffic. Abstractly, we can refer to these as workload. Similarly, the workload handling logic is hosted in cell sites, whereas in the other scenario, user workload is handled in data centers. A “larger” network site can handle more traffic. A larger site, at the same time, would be more expensive and might consume more electrical power, too. So, if you want to serve more users, you would need to appropriately equip the network sites. The workload handling capacity of a cell site is determined by the number of TRXs installed at it. Similarly, the workload handling capacity of a data center is determined by the number of servers installed in it. We can generically refer to these elements of workload handling as “network resources”.
Naturally, these sites costs money, so let’s get a feel for the kind of numbers we’re looking at.

## Slide 7: Lack of Energy Proportionality
Workload
Real Network
Ideal Network
Network power consumption is much higher than ideal except when workload peaks
Workload is much lower than peak most of the time
Networks are mostly under-utilized and have a high energy overhead compared to ideal
Energy inefficiency
Power consumption (Watt)
Notes: It turns out that networks such as cellular networks and geo-diverse data centers lack energy proportionality. As shown in this figure, the network power consumption is nearly independent of workload. Ideally, the network should consume zero power when there is zero workload. However, real life is far from ideal. So, as we assign workload to use cheaper electricity, we are playing with the limited swing available in the real network’s profile. We are reducing power consumed purely due to workload at sites with more expensive energy. We are not reducing the idle power consumption, which is quite significant.
Notice that if the network operated at a workload nearly equal to peak capacity, it doesn’t matter whether power consumption is “practical” or “ideal”. However, workload is quite variable and peaks for a short duration only, before falling to a much lower trough. To meet the “rush hour” demand, the network must be provisioned according to peak workload, but its capacity is under-utilized most of the time. Thus, the network power consumption is much higher than ideal. Ideally, the network should be completely energy proportional, i.e., instantaneous power consumption should follow the same pattern as the customer workload, but the swing in power consumption is quite limited. Due to the significant overhead in power consumption, we say that today’s networks are energy inefficient.

## Slide 8: Summary – Network Similarities
Network sites: Data centers / BTSs
Sites consist of resources: Servers / TRXs
  Resources determine:
    Workload capacity
    Peak / idle power consumption
Power consumption is an affine function of workload
Workload has diurnal cycles
  Peak much higher than trough
Energy inefficiency
Notes: We can see several similarities with the data centers scenario. The network consists of network sites, i.e., BTSs. A site consists of resources, i.e., TRXs, which determine the traffic capacity as well as power consumption. The power consumption of the sites is also known to be an affine function of workload as for the data centers. The workload also has diurnal cycles with a peak that is much higher than the trough. The sites are also known to be energy inefficient.

## Slide 9: Thesis Statement
A generalized optimization problem formulation can be used to minimize energy costs in different networks. This formulation must jointly exploit WR and RP.

## Slide 10: Lowering Electricity Cost
Reduce bill by using
  Less electricity
  Cheaper electricity
Energy Consumed (e) | 285 Million kWh
Unit Price (p) | $0.7
Total Bill = e x p | $200 Million
Hardware consolidation
  May cut electricity consumption by upto 80% []
Upgrading to energy efficient hardware
Resource pruning
Notes: Electricity cost is the product of unit price of electricity and the amount of electrical energy consumed. The latter is an accumulation or integration of the power consumption. So, we could reduce electricity consumption by using cheaper electricity or by reducing the amount of electricity consumed. Let’s see how we may do each of these one by one.

## Slide 11: Using Cheaper Electricity
Sites
1
2
3
Electricity price
Workload relocation
Notes: Suppose that the network operator has three network sites. These sites could be data centers or they could be cell towers or some other type of site depending on the type of network you consider. These sites are geographically distributed as they generally are. Let’s use circles spread horizontally to represent the sites. Electricity price exhibits geo-diversity, so let’s use the y-axis to indicate the electricity price. Now, the way to save electricity cost by using cheaper electricity is as follows. Network workload is known to have diurnal cycles with peak that has a short duration and much lower trough. So, when you have low workload, you wouldn’t need all of the sites. So, you assign workload preferably to the site with the cheapest electricity. If that site reaches capacity and you still have some more workload, you’ll assign it to the site with the next cheapest electricity. And so on and so forth. Since workload only peaks for a short duration, chances are you will be using relatively cheaper electricity for a significant fraction of time.
But the problem with this approach is that networks lack energy proportionality which diminishes the benefits of smartly distributing workload to save electricity cost. What does that mean?

## Slide 12: A Better Strategy
Workload
Real Network
Ideal Network
Our playground when using cheaper electricity
Couldn’t do anything about this
Power consumption (Watt)
Sites
1
2
3
Electricity price
Servers
Storage
Power distribution
Cooling
Network
Some servers
Inelastic load
Elastic load
Notes: It turns out that networks such as cellular networks and geo-diverse data centers lack energy proportionality. As shown in this figure, the network power consumption is nearly independent of workload. Ideally, the network should consume zero power when there is zero workload. However, real life is far from ideal. So, as we assign workload to use cheaper electricity, we are playing with the limited swing available in the real network’s profile. We are reducing power consumed purely due to workload at sites with more expensive energy. We are not reducing the idle power consumption, which is quite significant.
Notice that if the network operated at a workload nearly equal to peak capacity, it doesn’t matter whether power consumption is “practical” or “ideal”. However, workload is quite variable and peaks for a short duration only, before falling to a much lower trough. To meet the “rush hour” demand, the network must be provisioned according to peak workload, but its capacity is under-utilized most of the time. Thus, the network power consumption is much higher than ideal. Ideally, the network should be completely energy proportional, i.e., instantaneous power consumption should follow the same pattern as the customer workload, but the swing in power consumption is quite limited. Due to the significant overhead in power consumption, we say that today’s networks are energy inefficient.

## Slide 13: Problem Formulation
Time intervals
1
2
3
Electricity price
Joint workload relocation and resource pruning
Notes: So, we’ll need to bring a time axis into play here. Electricity prices change only at discrete intervals, so we can consider the time axis to be slotted into time intervals. The sites are all placed horizontally in the same order for each time interval in the above figure. Now, we need to assign workload to each network site. This assignment can be done in a number of ways for each interval and due to geo diversity in electricity price, each assignment for a given interval can have a different electricity cost associated with it. In other words, we need to pick a state for all the network sites during each interval, where each state has a certain cost associated with it.
When going from one state to another in consecutive intervals, workload assigned to one site may need to be shifted over to another to consolidate the workload better to conserve power. We call this workload relocation
Due to workload relocation, there may also be some cost of transition between adjacent states. The optimal electricity cost, over the given time horizon, would correspond to finding the set of states for each interval such that the sum of state and transition costs is minimum.
This sort of optimization could be applied to any network as long as: the electricity cost for a network site during an interval is a convex function of the workload assigned to it and network sites or resources within them can be turned on/off during low workload.
Mathematically, it can be given as this optimization objective function. What constraints would this optimization be subject to?

## Slide 14: Constraints
Honor workload capacity of resources
All workload must be handled
To each cell its own
Notes: Well, first off, there’s the capacity constraint. That is, each network site has a workload handling capacity, which must be respected. Then, we must also ensure that all workload that is offered to the network is assigned to one network site or another. A particular network may have other constraints specific to it. For instance, in case of cellular networks, a call may not be assigned to a far off cell site.
Now that we know the problem qualitatively, let’s see how we can mathematically model it.

## Slide 15: Mathematical Model – State Cost
Network’s idle power consumption
Site i’s workload capacity
Site i’s idle power consumption
Site i’s peak power consumption
Slope of power consumption profile
Idling power
Workload dependent power
Normalize over Pmax and replace f = Pmin / Pmax
Incurred if some resources on site i are active
Number of active resource sets
Number of independent resource sets

## Slide 16: Two Case Studies
Parameter | Cellular network | Data centers
Network resource
Workload relocation
Resource pruning
Transition costs
TRX
Call hand off
Negligible
Servers
Client redirect
Server shutdown / idle / hibernate
(De)activation overheads
BTS Power Saving
Redirection latency and scenario specific costs
Modify DNS / routing / App layer redicect

## Slide 17: Experimental Setup
Workload from 3 popular Facebook apps
Electricity prices from 33 US locations
Simulated a week-long deployment plan
Compared RED-BL against various algorithms
Notes: To evaluate RED-BL for geo-diverse data centers, we performed a simulation study which had the following setup. We used workload from three popular Facebook applications and normalized the cumulative workload. We verified that the characteristics of the cumulative workload resemble that of the workload for thousands of servers in a Google data center. We collected day-ahead electricity prices for 33 locations across the USA and simulated a weeklong deployment plan for the data centers situated at these locations. We compared RED-BL against a number of algorithms.

## Slide 18: Algorithms
STATIC_MIN: Least average price
LI: Local Optimal with Idling
LO: LI ignoring transition costs
LD: Local Optimal with Deactivation
LS: Local Optimal with Selection
UNIFORM: Equally distribute workload
Notes: Let’s represent a deactivated data center using a dark circle and shading to represent the workload mapped to a data center. As a baseline, we used UNIFORM, which distributes workload equally amongst all data centers and does not deactivate any data centers. STATIC_MIN assumes one large data center at the location which has the least average price over the planning horizon and assigns all workload to it. LI/LO/LD/LS are greedy algorithms that distribute workload amongst the sites based on electricity price, in a “cheapest site first” policy. LI keeps sites with no workload idling. LO deactivates sites that are idle but does not factor the transition cost while calculating the total electricity cost of the solution. LD always deactivates idle sites, whereas LS picks the cheaper of the two choices: whether to deactivate an idle site or keep it idling.

## Slide 19: Cost Savings vs Over-provisioning
RED-BL close to ideal savings
Falsely predicts high savings
Actual savings 10.35% lower
50% over provisioning => 26% Savings

## Slide 20: Electricity Cost vs Transition Cost
Notes: As the magnitude of transition overheads compared to the cost of handling workload increases, we see that the percentage savings in electricity cost decrease for all algorithms. RED-BL achieves close to the ideal lower bound electricity cost savings, whereas the best variants of the greedy algorithm scale worse than RED-BL.

## Slide 21: Granular (De)activation
Can only (de)activate entire data center
Can (de)activate half a data center
Cost savings over full data center (de)activation
Opportunity for greater savings
Notes: Now, let’s see how RED-BL energy savings would improve if we allowed independent (de)activation of fixed size fractions of a data center. The extreme right handside of this graph represents the case where you can only (de)activate an entire data center at a time. This is 0% better than the standard “all or nothing” RED-BL, because it is the same thing. If we were able to (de)activate half a data center at a time, we could do about 2.5% better than standard RED-BL. If we were able to independently (de)activate 10% of a data center at a time, we could do 5% better than standard RED-BL. So, there is opportunity for greater savings with granular (de)activation and it has a linear trend.

## Slide 22: DVFS Instead of Deactivation
Notes: If, instead of shutting down an entire data center, we switch the servers into lower-power mode using DVFS techniques, the power savings might reduce, but the scheme would be more agile to workload variations. Here, we see that the power consumption drops linear as the power consumption is lowered with DVFS. If the server power consumption drops to 10% of the peak, the data center power consumption would be reduced by about 70%. Another data point is that if we put all “idle” servers at 50% power consumption, we achieve about 20% power reduction.

## Slide 23: Reserve Margin
Notes: To be prepared for some stray workload at data centers which we planned to deactivate, we’ll keep some servers on as reserve. As we increase the amount of serving capacity in reserve mode, the difference in power consumption will increase compared to the scenario where we did not keep any reserve capacity.
Exactly how much “stray” traffic we receive can’t be predicted. In this chart, the lower line shows the situation where we don’t receive any stray traffic at all. The power consumption in that case is purely due to servers idling. The upper line represents the situation where we need all the reserve capacity for handling stray traffic. The actual situation may be somewhere in between.

## Slide 24: Summary – Case Study I
Significant cost savings are possible using RED-BL
Finer granularity of resource (de)activation increases savings
Low-power mode instead of shutdown also helps considerably
Cost savings decrease sharply with reserve margin

## Slide 25: Case study II - Prior work
Shutdown BTSs [Marsan et. al., C. Peng et al.]
  Risk of user churn
Shutdown some frequencies [D. Tipper et al.]
  Similar to our approach
Notes: Marsan et al proposed to shutdown some BTSs during low traffic regimes. The problem with this approach is that it risks user churn which is something operators can’t afford in the present day competition. Tipper et al. proposed to shutdown some frequencies, which is part of what we propose, i.e., RP. In addition, we couple WR, i.e., call handoffs.

## Slide 26: Does Workload Relocation Help?
Assume that power saving is enabled if upto two calls are being served
Power saving
Power saving
Power saving
Handing off some calls may enable greater power savings
Notes: Consider this scenario with eight callers and three BTSs. Suppose for instance, that power saving can be enabled if there are upto two calls on a BTS. According to the default situation, only one BTS may be placed in power saving mode. However, if we hand off some of the calls without overwhelming any BTS, we may put two BTSs in power saving mode, resulting in greater energy savings. This motivates that RP in conjunction with WR can achieve greater savings in cellular networks. This optimization is a discrete optimization, which we have shown to be NP-Hard.

## Slide 27: Alternate Serving BTSs
Notes: But can we really hand off calls to achieve greater savings? The answer, from datasets collected from live networks, is yes. As we can see about 50% callers have 3 or more candidate BTSs.

## Slide 28: Experimental Setup
Call volume traces for 2 days at 26 urban BTSs
Trace driven simulation:
  Periodically obtain optimal call placement
  Place BTSs with low-traffic in power-saving mode

## Slide 29: BTS Power Consumption Models
Parameter | Value |  | 
 | Model 1 | Model 2 | Model 3
Idle Power (W) | 1425 | 2401.8 | 2341.5
Peak Power (W) | 1500 | 3887.5 | 2973.9
Power Saving per TRX (W) | 20 | 50 | 100

## Slide 30: Results: Power-Saving Feature Only
Energy savings | Model 1 | Model 2 | Model 3
Percentage | 4.73% | 5.43% | 12.89%
Daily energy savings (kWh) | 43.28 | 109.68 | 217.12
Country-wide daily savings -3100 sites (MWh) | 51.6 | 130.77 | 258.87

## Slide 31: Results: Power-Saving + Handoff Absolute Energy Savings (%)

## Slide 32: Results: Power-Saving + Handoff Absolute Energy Savings (kWh)

## Slide 33: Effect of Granular Deactivation
Granularity | Model 1 | Model 2 | Model 3
2-state | 5.38% | 6.29% | 14.94%
3-state | 6.81% | 7.73% | 18.62%
6-state | 8.70% | 9.65% | 23.37%

## Slide 34: A Randomized Algorithm
Pick this
While there are BTSs in high-power mode
  Pick a random BTS
  For each call being handled by this BTS
    Hand-over to a candidate BTS in low-power mode
Nope
Nope
Yup!
Power saving
Power saving

## Slide 35: Performance of Heuristic Algorithm

## Slide 36: Effect of Late Deactivation

## Slide 37: Case Study II - Summary
Traffic has limited geo-flexibility compared to data centers
No geo-diversity in electricity prices
Mere activation of power savings feature supported in hardware helps
RED-BL achieves greater savings even for relatively conservative settings

## Slide 38: Conclusions
Abstracted data centers and cellular networks
Similarity:
  May be modeled as sets of geo-diverse resources
Contrasts:
  Availability of geo-diversity in electricity prices
  Geo-flexibility in traffic
  Magnitude of transition costs

## Slide 39: Conclusions
Mapping of workload to resources => Network state
Network state has bearing on electricity cost
Model electricity cost minimization as an optimal state trajectory problem
Showed the problem to be NP-Complete in the two case studies
Studied the sensitivity of the problem to various parameters

## Slide 40: Questions and Answers

## Slide 41: List of Papers
Published:
  A simulation study of GELS for Ethernet over WAN, GLOBECOM 2007
  RED-BL: Energy solution for loading data centers, INFOCOM Mini-Conference, 2012
  Electricity cost efficient workload mapping, INFOCOM Computer Communications Workshop, 2013
  Low-Carb: Reducing energy consumption in operational cellular networks, GLOBECOM 2013
  RED-BL: Evaluating dynamic right sizing for data centers, Computer Networks, vol. 72, 2014
Submitted:
  Low-Carb: A practical scheme for improving energy efficiency in cellular networks